## Slide 1
SMALL PRECISION TOOLS
Wedge Auto-Draw Rules
Small Wire (SW) Wedge Series – AB16 Series – Rules
DOCUMENT NO.
AB16_REL_Rev1_08112026
DATE
2026-11-08
PREPARED BY
Youssef
STATUS
Draft

## Slide 2
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series - V-Groove with integrated feed hole :
AB16 Series – Construction : AB16 has one shank style : STYLE_STD , with SLB feature All the 3D models is based on the bellow sketches; these sketch has all the required dimension to construction the 3D models and drawings
annotation_top_plan | TD - TDF
annotation_right_plan | W–ISA–VW–VR–VRR–VRA–TL–B-GA-GD
annotation_front_plan | BA-T-FD-RA-RA2-RA2H-CA-ERL-ERD-FL-C-BR-FR-H-HA-FNA-F-BF-Y-G-CGR-CGD-VBL-VBLR-funnel_gap – foot_depth
Never delete those sketches
For foot_depth we need to calculate it based on with foot type we have : VG groove , foot_depth = GD For funnel_gap we have the equation , just in case of SLB feature make in the equation that BA = 0deg

## Slide 3
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB 3D for Customer / Production Drawings : PGB 3D has the following feature :
Always ON
Always ON
Optional if we have VR, VRA, VRR, VW
Optional if we have W2
Always ON
Optional if we have VBLR, VBL
Optional if we have RA2, RA2H

## Slide 4
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – FG 3D for Customer / Production Drawings: FG 3D has the following feature, We respect the rule of PGB but adding the bellow
Respect the PGB rules
Always ON
Always ON
Always ON
Always ON
Optional , based on hole type , we need to have H
Optional , based on hole type , we need to have HH, HW , you need to change H = HH
Optional , based on hole type , we need to have ST, SW, you need to change H=ST
Always ON , we need B, GA, GD
Optional , if we have CGO, CGR, G

## Slide 5
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – Customer / Production Drawings: We can select the type of drawing from drawings properties manager, PGB no need to fill these properties
Front view
Right view
Top view
Detail view
Section view

## Slide 6
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Customer / Production Drawings: Front view in case of PGB :
Front view have many annotation, all the annotation are from annotation_front_plan BA@annotation_front_plan BA_VBL@annotation_front_plan in case we have SLB feature The view can be positioned based on your preference

## Slide 7
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Customer / Production Drawings: Right view in case of PGB :
Right view have many annotation, all the annotation are from annotation_right_plan
TL@annotation_right_plan
VR@annotation_right_plan Optional
The view can be positioned based on your preference

## Slide 8
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Customer / Production Drawings: Top view in case of PGB :
Top view have many annotation, all the annotation are from annotation_top_plan TD@annotation_top_plan TDF@annotation_top_plan The view can be positioned based on your preference

## Slide 9
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Customer / Production Drawings: Detail view in case of PGB :
Detail view have many annotation, all the annotation are from annotation_right_plan W@annotation_right_plan ISA@annotation_right_plan VW@annotation_right_plan Optional VRA@annotation_right_plan Optiona W2@annotation_righ_plan Optional l The view can be positioned based on your preference

## Slide 10
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Customer / Production Drawings: Section view in case of PGB :
Section view have many annotation, all the annotation are from annotation_front_plan In case of SYLE_A we show only : FL@annotation_front_plan
T@annotation_front_plan The view can be positioned based on your preference

## Slide 11
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – FG Customer / Production Drawings: Front view in case of FG :
Front view have many annotation, all the annotation are from annotation_front_plan BA@annotation_front_plan BA_VBL@annotation_front_plan in case we have SLB feature The view can be positioned based on your preference

## Slide 12
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – FG Customer / Production Drawings: Right view in case of FG :
Right view have many annotation, all the annotation are from annotation_right_plan
TL@annotation_right_plan
VR@annotation_right_plan Optional
The view can be positioned based on your preference

## Slide 13
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – FG Customer / Production Drawings: Top view in case of FG :
Top view have many annotation, all the annotation are from annotation_top_plan TD@annotation_top_plan TDF@annotation_top_plan The view can be positioned based on your preference

## Slide 14
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – FG Customer / Production Drawings: Detail view in case of PGB :
Detail view have many annotation, all the annotation are from annotation_right_plan W@annotation_right_plan W2@annotation_right_plan Optional ISA@annotation_right_plan VW@annotation_right_plan Optional VRA@annotation_right_plan Optional B@annotation_right_plan
GA@annotation_right_plan
GD@annotation_right_plan
The view can be positioned based on your preference

## Slide 15
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – FG Customer / Production Drawings: Section view in case of PGB :
Section view have many annotation, all the annotation are from annotation_front_plan FL@annotation_front_plan
T@annotation_front_plan
FNA@annotation_front_plan
HA@annotation_front_plan
H@annotation_front_plan HH@annotation_front_plan Optional if oval hole ST@annotation_front_plan Optional if slot hole
FR@annotation_front_plan
BR@annotation_front_plan
BF@annotation_front_plan only in production drawing
F@annotation_front_plan only in production drawing
Y@annotation_front_plan only in production drawing CGD@annotation_front_plan
CGR@annotation_front_plan only in production drawing
G@annotation_front_plan The view can be positioned based on your preference

## Slide 16
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series –Overlay : Construction of overlays
In general, overlays respect the following shape : Right and Left view. Axillary view Optional Annotation Overlay Metadata controlled by properties manager's bellow
Right view
Left view
Axillary view
Annotation

## Slide 17
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series –Overlay : Construction of overlays std_shank case :
View will pe positioned based on reference points :
std_ref_point_right will control the cut of the right view in the overlay; the right view is already assigned the righ_view configuration . The control of the cut is done by the programmer based by changing the value of std_ref_point_right@std_ref_point_right based on the cases we have . The old cut was based on the scale of the view was : std_ref_point_right@std_ref_point_right = 2.01175in/ "scale“ this is OK for most of standard cases but for cases with VR its no OK the programmer will need to give the appropriate value
std_ref_point_left will control the cut of the right view in the overlay; the right view is already assigned the left_view configuration . The control of the cut is done by the programmer based by changing the value of std_ref_point_left@std_ref_point_left based on the cases we have . The old cut was based on the scale of the view was : std_ref_point_left@std_ref_point_left = 2.01175in/ "scale“ this is OK for most of standard cases

## Slide 18
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series –Overlay : Construction of overlays
Right & Left view will have the same scale; the scale is chosen based on FL values
Numerical Limits:
x400 : T ≤ 0.0134 in or 0.3403 mm
x300 : T ≤ 0.0180 in or 0.4572 mm
x200 : T ≤ 0.0272 in or 0.6908 mm
x100 : T ≤ 0.0542 in or 1.3766 mm The scales : S100 = 1:60.8
S200 = 1:121.1
S300 = 1:183.0
S400 = 1:246.0

## Slide 19
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Overlay : Construction of PGB overlays std_shank
Note 1 : The programmer need to change the values of the parameters in equation & inside the sketches based of above
Change W to MAX values & W_MIN inside the sketch
Turn off
If VW=W , Change VW , VRA to MAX & VR to MIN & VW_MIN , VRA_MIN, VRA_MAX inside the sketch
If VW≠W , Change VW , VRA, W, ISA to MAX & VR to MIN & VW_MIN , VRA_MIN, VRA_MAX, W_MIN, ISA_MIN
Change T, FD to MAX & T_MIN. FD_MIN inside sketch this the standard case
If SLB, Change T, FD to MAX & T_MIN. FD_MIN inside sketch
If RA2, Change T, FD,RA2H to MAX & T_MIN. FD_MIN, RA2H_MIN inside sketch
If RA2 & SLB, Change T, FD,RA2H to MAX & T_MIN. FD_MIN, RA2H_MIN inside sketch
Turn off

## Slide 20
Rules
SMALL PRECISION TOOLS
Confidential
AB16 Series – PGB Overlay : Construction of PGB overlays std_shank
Note 1 : The programmer need to change the values of the parameters in equation & inside the sketches based of above
Change W to MAX values & W_MIN inside the sketch
Change inside the sketch W_MIN, W_MAX , W parameter remain nominal
If VW=W , Change VW , VRA to MAX & VR to MIN & VW_MIN , VRA_MIN, VRA_MAX inside the sketch
If VW≠W , Change VW , VRA, W, ISA to MAX & VR to MIN & VW_MIN , VRA_MIN, VRA_MAX, W_MIN, ISA_MIN
Change T, FD to MAX & T_MIN. FD_MIN inside sketch this the standard case
If SLB, Change T, FD to MAX & T_MIN. FD_MIN inside sketch
If RA2, Change T, FD,RA2H to MAX & T_MIN. FD_MIN, RA2H_MIN inside sketch
If RA2 & SLB, Change T, FD,RA2H to MAX & T_MIN. FD_MIN, RA2H_MIN inside sketch
B, GA, GD to MIN values & B_MAX, GA_MAX, GD_MAX