## Slide 1
SMALL PRECISION TOOLS
Wedge Auto-Draw Rules
Small Wire (SW) Wedge Series – VM Series – Rules
DOCUMENT NO.
VM_REL_Rev1_09272026
DATE
2026-09-27
PREPARED BY
Youssef
STATUS
Draft

## Slide 2
VM Series – Overview & Construction
SMALL PRECISION TOOLS
Confidential
VM Series – Autobonding: The VM series combines all standard wedge features with a cavity-guide design, widely used for small aluminum wire bonding. Its elliptical back radius keeps the wire centered in the tool for more accurate bond placement.
VM Series – Construction: Shank style: STYLE_STD, with the optional SLB feature. All 3D models are built from the sketches below, which hold every dimension needed for the 3D models and drawings.
Never suppress these features!
foot_depth depends on the foot type:} {VG groove: foot_depth = GD} {C groove: foot_depth = CD} {G groove: foot_depth = GD} {Flat W: foot_depth = 0
funnel_gap is driven by an equation. When the SLB feature is active, set BA = 0° in that equation.

## Slide 3
VM Series – VRA Angle Rule
SMALL PRECISION TOOLS
Confidential
VM Series – VRA angle: Additional VRA angle rules, per the latest update from SPT.
The arrow shows where the VRA angle is placed. If the database gives VRA = 90°, the program must enter 0°. Otherwise, use the VRA value from the database. The 90° angle at the top is fixed – do not change it. The annotation name is unchanged, so drawing positioning still works. For the VR option, also see the overlay changes on the last slides.

## Slide 4
PGB 3D Model – Features
SMALL PRECISION TOOLS
Confidential
VM Series – PGB 3D model (Customer / Production drawings): Features for the standard shank case:
Always ON – requires TD, TDF
Always ON – requires W, ISA
Always ON – requires FD, T, RA, BA
Optional – requires VR, VRA, VW, VRR
Optional – requires VBL, VBLR, T
Always ON – requires C, ND, NR, NA, FTA

## Slide 5
FG 3D Model – Features & Wire Exit
SMALL PRECISION TOOLS
Confidential
VM Series – FG 3D model (Customer / Production drawings): Features for the standard shank case:
Optional – requires W2
Optional – requires RA2, RA2H
Optional – requires FRO
Always ON – requires ID, IDTD, IDFA
Standard hole wire exit (optional): activate all these features – requires H, HA, Y, FNA, funnel_gap
Oval hole wire exit (optional): activate all these features – requires HW, HH, HA, Y, FNA, funnel_gap
Slot wire exit (optional): activate all these features – requires SW, ST, Y, FNA, funnel_gap
Optional – only if TIP is in the DB
Always ON – requires NR

## Slide 6
FG 3D Model – Groove Features
SMALL PRECISION TOOLS
Confidential
VM Series – FG 3D model (Customer / Production drawings): Groove features for the standard shank case:
VG groove (optional): activate all these features – requires GA, GD
G groove (optional): activate all these features – requires GO, GD
C groove (optional): activate std_c_feature, then: – FRO = FR: activate std_br_c_feature – FRO ≠ FR: activate std_br_c_feature + std_c_fr_feature C + CBR: activate std_cbr_c_feature + std_cbr_c_core_feature, or std_cbr_c_feature + std_c_fr_feature, depending on FRO vs FR. CBR requires CBRL and CBRD.
F groove (optional): activate all these features – requires FR, BR; FRO must be OFF

## Slide 7
Drawings – Drawing Type & Views
SMALL PRECISION TOOLS
Confidential
VM Series – Customer / Production drawings: Pick the drawing type in the Properties Manager (not needed for PGB).
Front view
Right view
Top view
Detail view
Section view

## Slide 8
PGB Drawing – Front View
SMALL PRECISION TOOLS
Confidential
VM Series – PGB Customer / Production drawings: Front view (PGB)
All annotations in this view come from annotation_std_front_plan. For STYLE_STD, show only: BA@annotation_std_front_plan VBL@annotation_std_front_plan – only with the SLB feature BA_SLB@annotation_std_front_plan – only with the SLB feature The view can be placed wherever you prefer.

## Slide 9
PGB Drawing – Right View
SMALL PRECISION TOOLS
Confidential
VM Series – PGB Customer / Production drawings: Right view (PGB)
All annotations in this view come from annotation_right_plan. TL@annotation_right_plan VR@annotation_right_plan – optional The view can be placed wherever you prefer.

## Slide 10
PGB Drawing – Top View
SMALL PRECISION TOOLS
Confidential
VM Series – PGB Customer / Production drawings: Top view (PGB)
All annotations in this view come from annotation_top_plan. TD@annotation_top_plan TDF_STD@annotation_top_plan – standard shank only The view can be placed wherever you prefer.

## Slide 11
PGB Drawing – Detail View
SMALL PRECISION TOOLS
Confidential
VM Series – PGB Customer / Production drawings: Detail view (PGB)
All annotations in this view come from annotation_right_plan. W@annotation_right_plan ISA@annotation_right_plan VW@annotation_right_plan – optional VRA@annotation_right_plan – optional The view can be placed wherever you prefer.

## Slide 12
PGB Drawing – Section View
SMALL PRECISION TOOLS
Confidential
VM Series – PGB Customer / Production drawings: Section view (PGB)
All annotations in this view come from annotation_std_front_plan. For STYLE_STD, show only: FL@annotation_std_front_plan T@annotation_std_front_plan The view can be placed wherever you prefer.

## Slide 13
FG Drawing – Front View
SMALL PRECISION TOOLS
Confidential
VM Series – FG Customer / Production drawings: Front view (FG)
All annotations in this view come from annotation_std_front_plan. For STYLE_STD, show only: BA@annotation_std_front_plan VBL@annotation_std_front_plan – only with the SLB feature BA_SLB@annotation_std_front_plan – only with the SLB feature The view can be placed wherever you prefer.

## Slide 14
FG Drawing – Top View
SMALL PRECISION TOOLS
Confidential
VM Series – FG Customer / Production drawings: Top view (FG)
All annotations in this view come from annotation_top_plan. TD@annotation_top_plan TDF_STD@annotation_top_plan RD1@Drawing View3 – hole annotation The view can be placed wherever you prefer.

## Slide 15
FG Drawing – Right View
SMALL PRECISION TOOLS
Confidential
VM Series – FG Customer / Production drawings: Right view (FG)
All annotations in this view come from annotation_right_plan. TL@annotation_right_plan VR@annotation_right_plan – optional TIP@annotation_right_plan – optional The view can be placed wherever you prefer.

## Slide 16
FG Drawing – Detail View
SMALL PRECISION TOOLS
Confidential
VM Series – FG Customer / Production drawings: Detail view (FG)
All annotations in this view come from annotation_right_plan. W@annotation_right_plan ISA@annotation_right_plan W2@annotation_right_plan – W2 option only VW@annotation_right_plan – VR option only VRA@annotation_right_plan – VR option only B@annotation_right_plan – VG groove only GA@annotation_right_plan – VG groove only GD@annotation_right_plan – VG groove only GD_G@annotation_right_plan – G groove only GO@annotation_right_plan – G groove only CL@annotation_right_plan – C groove only CD@annotation_right_plan – C groove only The view can be placed wherever you prefer.

## Slide 17
FG Drawing – Section View
SMALL PRECISION TOOLS
Confidential
VM Series – FG Customer / Production drawings: Section view (FG, standard shank)
Annotations come from annotation_std_front_plan, except the production-only ones. Always show (@annotation_std_front_plan): FL, T, RA, C, NA, FTA, ND, NR, FNA, HA, FRO Show only when it applies (@annotation_std_front_plan): RA2 – RA2 option H – standard hole HH – oval hole ST – slot FR – hide when FRO = FR BR – hide when CBR is present Production drawing only (@annotation_front_plan): BF, F, Y, CBRL, CBRA The view can be placed wherever you prefer.

## Slide 18
Overlays – Layout
SMALL PRECISION TOOLS
Confidential
VM Series – Overlays: How an overlay is built
Every overlay follows this layout: Right and left views Auxiliary view (optional) Annotation Overlay metadata – set in the Properties Manager (below)
Right view
Left view
Auxiliary view
Annotation

## Slide 19
Overlays – Reference Points (Std Shank)
SMALL PRECISION TOOLS
Confidential
VM Series – Overlays: Overlay construction, std_shank case
Views are positioned using reference points:
std_ref_point_right controls where the right view is cut in the overlay (the right view uses the right_view configuration). The programmer sets the cut for each case by changing std_ref_point_right@std_ref_point_right. Previous rule, based on the view scale: std_ref_point_right@std_ref_point_right = 2.01175 in / scale OK for most standard cases, but not OK for VR cases – the programmer must set the correct value.
std_ref_point_left controls where the left view is cut in the overlay (the left view uses the left_view configuration). The programmer sets the cut for each case by changing std_ref_point_left@std_ref_point_left. Previous rule, based on the view scale: std_ref_point_left@std_ref_point_left = 2.01175 in / scale OK for most standard cases.

## Slide 20
Overlays – Reference Points (Rev Shank)
SMALL PRECISION TOOLS
Confidential
VM Series – Overlays: Overlay construction, rev_shank case
Views are positioned using reference points:
rev_ref_point_right controls where the right view is cut in the overlay (the right view uses the right_view configuration). The programmer sets the cut for each case by changing rev_ref_point_right@rev_ref_point_right. Previous rule, based on the view scale: rev_ref_point_right@rev_ref_point_right = 2.01175 in / scale OK for most standard cases, but not OK for VR cases – the programmer must set the correct value.
rev_ref_point_left controls where the left view is cut in the overlay (the left view uses the left_view configuration). The programmer sets the cut for each case by changing rev_ref_point_left@rev_ref_point_left. Previous rule, based on the view scale: rev_ref_point_left@rev_ref_point_left = 2.01175 in / scale OK for most standard cases.

## Slide 21
Overlays – Scale Selection
SMALL PRECISION TOOLS
Confidential
VM Series – Overlays: Scale selection
Right and left views use the same scale, chosen from the FL value.
Limits per scale:
x400: T ≤ 0.0134 in (0.3403 mm)
x300: T ≤ 0.0180 in (0.4572 mm)
x200: T ≤ 0.0272 in (0.6908 mm)
x100: T ≤ 0.0542 in (1.3766 mm)
Scale values:
S100 = 1:60.8
S200 = 1:121.1
S300 = 1:183.0
S400 = 1:246.0

## Slide 22
PGB Overlay – Sketch Settings
SMALL PRECISION TOOLS
Confidential
VM Series – Overlays: PGB overlay sketches, std_shank
Note: the programmer must apply these values both in the equations and inside the sketches.
W → MAX. Sketch: W_MIN
Turn off
If VW = W: VW, VRA → MAX; VR → MIN. Sketch: VW_MIN, VRA_MIN, VRA_MAX
If VW ≠ W: VW, VRA, W, ISA → MAX; VR → MIN. Sketch: VW_MIN, VRA_MIN, VRA_MAX, W_MIN, ISA_MIN
Standard case: T, FL → MAX; ND, C → MIN. Sketch: T_MIN, FL_MIN, C_MAX, ND_MAX
If SLB: T, FL → MAX; ND, C → MIN. Sketch: T_MIN, FL_MIN, C_MAX, ND_MAX
If RA2: T, FL → MAX; ND, RA2H → MIN. Sketch: T_MIN, FL_MIN, RA2H_MAX, ND_MAX
If RA2 + SLB: T, FL → MAX; ND, RA2H → MIN. Sketch: T_MIN, FL_MIN, RA2H_MAX, ND_MAX
Turn off
Turn off
Turn off

## Slide 23
FG Overlay – Sketch Settings
SMALL PRECISION TOOLS
Confidential
VM Series – Overlays: FG overlay sketches, std_shank
Note: the programmer must apply these values both in the equations and inside the sketches.
W → NOM. Sketch: W_MIN, W_MAX
Turn off
If VW = W: VW, VRA → MAX; VR → MIN. Sketch: VW_MIN, VRA_MIN, VRA_MAX
If VW ≠ W: VW, VRA, W, ISA → MAX; VR → MIN. Sketch: VW_MIN, VRA_MIN, VRA_MAX, W_MIN, ISA_MIN
Standard case: T, FL → MAX; ND, C → MIN. Sketch: T_MIN, FL_MIN, C_MAX, ND_MAX
If SLB: T, FL → MAX; ND, C → MIN. Sketch: T_MIN, FL_MIN, C_MAX, ND_MAX
If RA2: T, FL → MAX; ND, RA2H → MIN. Sketch: T_MIN, FL_MIN, RA2H_MAX, ND_MAX
If RA2 + SLB: T, FL → MAX; ND, RA2H → MIN. Sketch: T_MIN, FL_MIN, RA2H_MAX, ND_MAX
If C groove: CL, CD → MIN. Sketch: CL_MAX, CD_MAX
If VG groove: GA, GD, B → MIN. Sketch: GA_MAX, GD_MAX, B_MAX
If G groove: GO, GD → MIN. Sketch: GO_MAX, GD_MAX