## Slide 1
SMALL PRECISION TOOLS
Wedge Auto-Draw Requirements
Large Wire (LW) Wedge Series – 4516/3016 Requirements
DOCUMENT NO.
4516_REQ_Rev0_07152026
DATE
2026-15-07
PREPARED BY
Youssef
STATUS
Draft

## Slide 2
Scope
This document defines the production drawing, customer drawing, and overlay requirements for the 4516 series, covering both the finished wedge and the Pre-Ground Blank (PGB).Including 4516 , 4510, 4515
SMALL PRECISION TOOLS
Confidential
04

## Slide 3
Tool Overview
4516 Series — 60° V-Groove with integrated feed hole (L-notch tool)
Wire feed angle: 45°
Wire size range: 75–500 microns (3–20 mils)
SMALL PRECISION TOOLS
Confidential
04

## Slide 4
Configuration Options
Shank: SW_STD with SLB feature
SMALL PRECISION TOOLS
Confidential
04
For Tip detail we have STD 20°ISA , WITH VW VR

## Slide 5
Configuration Options
Foot options: SW_C, SW_F, SW_CG, SW_G, SW_VG, SW_CC
SMALL PRECISION TOOLS
Confidential
04

## Slide 6
Configuration Options
Notch type: SW_Notch
SMALL PRECISION TOOLS
Confidential
04
Note : Some cases we may have ERW, ERD, FLER & CA

## Slide 7
Configuration Options
Feed hole types: STD (Round), Oval, Slot
SMALL PRECISION TOOLS
Confidential
04
Note : Y will be used to position the hole

## Slide 8
Configuration Options
BR feature: Round BR
SMALL PRECISION TOOLS
Confidential
04
Note : Round BR only used in case when we have ERW, ERD, FLER & CA

## Slide 9
Database Requirements
Schema is largely consistent with the COB tool family.Additional fields required, including NR.TBD: full list of new/changed fields pending.
SMALL PRECISION TOOLS
Confidential
04
Part_Spec | PN | Filter | Drawing_Number | Description_2 | Wed-Type | Wed-Foot_Option | Wed-Wire_Exit | Wed-Feed_H/Slot | Wed-FG-Style
116823 | 3112854 |  | 22000042 | 4516-10L-W-3MM-1.00-G | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116827 | 3112855 |  | 22000747 | 4516-12R-W-3MM-1.00-G | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116828 | 3112859 |  | 22000977 | 4516-3R-W-1/16-1.200-GM FR=0012 BR=002 FL=0067 W=0055 TDF=046 | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116841 | 3112860 |  | 22001068 | 4516-3S-W-1/16-1.00-GP FL=0085 H=004 GD=001 B=0023 F=004 | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116847 | 3112862 |  | 22001068 | 4516-3S-W-1/16-1.20-G FL=0085 H=004 GD=001 B=0023 F=004 | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
139860 | 3112865 |  | 22000502 | 4516-3XL-W-1/16-1.00-G | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116835 | 3112866 |  | 22000502 | 4516-3XL-W-1/16-1.00-GP | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116837 | 3112867 |  | 22000049 | 4516-3XL-W-1/16-1.00-GP FL=.011 W=.0067 | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116838 | 3112868 |  | 22000502 | 4516-3XL-W-1/16-1.200-G TDF=.046 | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116843 | 3112869 |  | 22001154 | 4516-3XL-W-1/16-1.20-GP FL=.011 TDF=.046 W=.0067 DWG-22001154-DW | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
116836 | 3112870 |  | 22000003 | 4516-3XL-W-1/16-1.225-GP EP FFP TDF=.046 | LW_std_HOLE | LW_G | SW_L-Notch | STD(Round) | 4516
Note : There are some missing parameters needed to be added to database like NR

## Slide 10
Customer Drawing Requirements
For customer drawing we will replicate as the same provided, following the same step as COB
SMALL PRECISION TOOLS
Confidential
04
Front, Right & Top Views
Detail & Section Views
Dimensions Tables

## Slide 11
Production Drawing Requirements
For customer drawing we will replicate as the same provided, following the same step as COB
SMALL PRECISION TOOLS
Confidential
04
Front, Right & Top Views
Detail & Section Views
Dimensions Tables
Add all dimensions and parameters to views

## Slide 12
Overlay Requirements: Finish Wedge
Similar to COB overlay, with different tolerance zone construction. Special case: view must focus on the top of the part only — scale selection may need to change accordingly.
SMALL PRECISION TOOLS
Confidential
04
Note : Scaling the view the same way as COB will not work for 4516/3016 Note : Only add two views to the overlays Note : No need to all the annotations

## Slide 13
Overlay Requirements: PGB
Remains unchanged from the standard wedge overlay used across all tool families.
SMALL PRECISION TOOLS
Confidential
04
Note : PGB overlay may have VR/VW feature