## Slide 1
SMALL PRECISION TOOLS
Wedge Auto-Draw Requirements
Small Wire (SW) Wedge Series – M Series – Microwave Bonding Tools
Requirements
DOCUMENT NO.
M_REQ_Rev0_07202026
DATE
2026-21-07
PREPARED BY
Youssef
STATUS
Draft

## Slide 2
Scope
This document defines the production drawing, customer drawing, and overlay requirements for the M Series – Microwave Bonding Tools
Requirements series, covering both the finished wedge and the Pre-Ground Blank (PGB). Including M45A, M45B
SMALL PRECISION TOOLS
Confidential
04

## Slide 3
Tool Overview
SMALL PRECISION TOOLS
Confidential
04

## Slide 4
Configuration Options
Shank: SW_STD with SLB feature , SW_180REV with SLB feature
SMALL PRECISION TOOLS
Confidential
04
For Tip detail we have STD 20°ISA , WITH VW VR , CHMFERED W2, 10°BA, 0°BA, SECOND RA2

## Slide 5
Configuration Options
Foot options: SW_C, SW_F, SW_CG, SW_G, SW_VG, SW_CC
SMALL PRECISION TOOLS
Confidential
04

## Slide 6
Configuration Options
Notch type: SW_L-Notch,
SMALL PRECISION TOOLS
Confidential
04
Note : No need for the C value

## Slide 7
Configuration Options
Feed hole types: STD (Round), Oval, Slot
SMALL PRECISION TOOLS
Confidential
04
Note : Y will be used to position the hole

## Slide 8
Configuration Options
BR feature: N/A
SMALL PRECISION TOOLS
Confidential
04
Note :

## Slide 9
Database Requirements
Schema is largely consistent with the COB tool family.
SMALL PRECISION TOOLS
Confidential
04
Note : We may need to add the fields like Wedge type; Foot type; etc. Note : We will need to add some rules of data handling !
Part_Spec | PN | Filter | Drawing_Number | Description_2 | Wed-Type | Wed-Foot_Option | Wed-Wire_Exit | Wed-Feed_H/Slot
117627 | 3112545 |  | 14003377 | M45A-WH-1510-3/4-F | SW_STD | SW_F | SW L Notch | STD(Round)
117625 | 3112546 |  | 14003377 | M45A-WH-1510-S-F W=.003 | SW_STD | SW_F | SW L Notch | STD(Round)
117641 | 3112756 |  | 14001389 | M45A-TI-1515-S-FM W=003 | SW_STD | SW_F | SW L Notch | STD(Round)
117802 | 3112760 |  | 14003533 | M45A-TI-2020-S-FM | SW_STD | SW_F | SW L Notch | STD(Round)

## Slide 10
Customer Drawing Requirements
For customer drawing we will replicate as the same provided, following the same step as COB
SMALL PRECISION TOOLS
Confidential
04
Front, Right & Top Views
Detail & Section Views
Dimensions Tables
Note : Noticed the VFL has an angle, but Not define in the DB

## Slide 11
Production Drawing Requirements
For customer drawing we will replicate as the same provided, following the same step as COB
SMALL PRECISION TOOLS
Confidential
04
Front, Right & Top Views
Detail & Section Views
Dimensions Tables
Add all dimensions and parameters to views
Note : The production drawing will follow the same as sample provided

## Slide 12
Overlay Requirements: Finish Wedge
Like COB overlay, with different tolerance zone construction. .
SMALL PRECISION TOOLS
Confidential
04
Note : Scaling the view the same way as COB, The T dimension start from TDF Note : Only add two views to the overlays Note : No need to all the annotations

## Slide 13
Overlay Requirements: PGB
Remains unchanged from the standard wedge overlay used across all tool families. Feed Hole added
SMALL PRECISION TOOLS
Confidential
04
Note : The PGB may have the VR/VW version !